Power Grid Analysis with Applications to Power Grid Security

---
Why Do we care?
A failure in a line causes stress on the power grid.
When looking at the transient after failing a line, we can see other power line reach a flow higher than the lines capacity.
These additional failures can lead to a cascading failure.

---
Power Grid Analysis
Swing Equation:
A line will fail if the power exceeds the threshold flow.
ddot%theta_I =P_i- %gamma_i dot%theta + %SIGMA_j K_ij sin(%theta_j-%theta_i )
flow= K_ij sin( %theta_j-%theta_i )
%alpha %element [0,1] newline{} %alpha K_ij<K_ij sin( %theta_j-%theta_i)

---
Example of a Line Failure
An example showing the transient after a line failure.
We can see how power flow jump much larger than the steady state.

---
Linear Swing equation
Now we look at a linear swing equation:
The results of the transient is similar to the nonlinear swing equitation in the networks we are viewing.
ddot%theta_I =P_i- %gamma_i dot%theta + %SIGMA_j K_ij(%theta_j-%theta_i )

---
Linearizing The Swing Equation
We now look at the linear swing equation.
Now we diagonalize L. Where V is the eigenvector matrix and Λ is a matrix with the eigenvalues along the main diagonal.
We now set
And get
We can break up this equation
%eta(t) =V^-1%theta(t) newline{ } Q=V^-1P
ddot%theta(t) =P- %gamma dot%theta(t) + L%theta(t) newline{ } newline{ } Where~L~is~the~Laplacian~"matrix"
ddot%eta( t )=Q -%gamma dot%eta(t) - %LAMBDA %eta( t )
ddot%eta_i( t )=Q_i -%gamma dot%eta_i(t) - %lambda_i %eta_i( t )
L= V %LAMBDA V^-1 newline{ }

---
Linearize Swing Equation
We now have decoupled the systems. We can now analyze eta independently of other etas
To get back theta we use:
%theta_i(t)= %SIGMA_J V_ij %eta_j( t ) newline{ } newline{ } flow = sin( %theta_j -%theta_i )

---
Conclusion
Gaining an understanding of the transient response will help to identify nodes of a network that will lead to a cascading failure.
Knowing nodes that vulnerable, allow for better security of the power grid. Allowing for more security of vulnerable nodes to protect the grid from Cyber attacks

---
References
Title:Dynamically induced cascading failures in power grids
- Schäfer, B., Witthaut, D., Timme, M. et al. Dynamically induced cascading failures in power grids. Nat Commun 9, 1975 (2018). https://doi.org/10.1038/s41467-018-04287-5